## Slide 1: Motivation
Human-Robot Interaction, Virtual Reality: pointing based interaction suitable
  Use hand postures to add expressiveness
Designer challenge: which hand postures are the best for
  Performance?
  User Experience?

## Slide 2: Study Goal
Problem
Hand posture evaluation either subjective or work intensive
Hypothesis
Hand posture comfort and discomfort affect performance and obviously user experience
Goals
Create a metric for quick and objective hand posture comfort/discomfort evaluation
Show its effect on performance in a pointing task

## Slide 3: Related Work: Comfort and Discomfort (Vink et al.)
Comfort
“pleasant state or relaxed feeling of a human being”
Influenced by subjective impressions and expectations
Discomfort
“an unpleasant state of the human body”
Caused by physical stress

## Slide 4: Related Work
Apostolico et al:
Introduce and determine the Range of Rest Posture for human joints (later more)
Naddeo et al:
Propose a quantitative method for postural comfort evaluation
Comfort based on the distance to the range of rest posture
But: complex computation, limited to comfort

## Slide 5: Hand Comfort/Discomfort Components
Four components affect hand comfort/discomfort:
Deviation from Range of Rest Posture (RRP)
Inter Finger Angles (IFA)
Finger Hyperextension (HE)
Finger Abduction (FA)

## Slide 6: Hand Comfort/Discomfort Components
Deviation from Range of Rest Posture (RRP)
Apostolico et al:
Every joint has a rest posture
When in the rest posture, maximum comfort is perceived
  Deviation from rest posture should decrease comfort
Due to anatomical differences: look at Range of Rest Posture
In our case: look at the RRPs for all hand joints

## Slide 7: Hand Comfort/Discomfort Components
Inter Finger Angles (IFA)
Complex Hand Anatomy:
Finger extendors and flexors share same muscles
Inter-finger tendons
  Individual finger movement limited
High inter finger angle differences create stress on tendons, muscles
  Discomfort

## Slide 8: Hand Comfort/Discomfort Components
Finger Hyperextension (HE)
LaViola et al. : “[hyperextension] puts more strain on the [MCP] joints and tendons than the hand is accustomed to”
  High stress on joints, tendons, muscles
  Discomfort

## Slide 9: Hand Comfort/Discomfort Components
Finger Abduction (FA)
Analog to hyperextension:
High abduction creates stress on joints, tendons, muscles, soft tissue
  Discomfort

## Slide 10: Concrete Implementation: RRP Metric Comp.
Hand Model:
21 DOF Angle Based Hand
Interpret Hand as a vector of length 21
In Theory:
There is a RRP for each DOF
  Identify RRP for each DOF
  For a particular hand posture, add up the distances to the RPP for each joint
1
2
1
2
1
2
1
2
1
1
1
1
3
1
1

## Slide 11: Concrete Implementation: RRP Metric Comp.
For simplicity:
Define RRP for whole hand as a set of 50 relaxed hand postures
Calculate minimum Euclidian distance to RRP set for particular hand
  Yields RRP component for whole hand
Metric value 0: maximum comfort
Perceived comfort decreases when metric value increases

## Slide 12: Concrete Implementation: RRP Metric Comp.

## Slide 13: Combining the Metric Components
In order to make comparable:
  Metric value = 0 → maximum comfort, minimum discomfort
  Metric increases → comfort decreases, discomfort increases
Add the component values
Weight with importance coefficients

## Slide 14: Combining the Metric Components
Naïve Metric
whole hand component values
importance coefficients empirically estimated
Simple implementation, gives good rough estimate of comfort/discomfort
But: ignores anatomical differences of individual fingers

## Slide 15: Combining the Metric Components
Improved Metric
Compute the metric components for each finger, weight finger components individually
Instead of estimating coefficients:
  Collect data in user study (with help of naïve metric)
  Use machine learning (least squares) to find optimal coefficients

## Slide 16: User Study
Objectives for User Study:
Gather data for improving metric
Verify that improved metric reflects perceived user comfort and discomfort
Show that comfort/discomfort affect performance in pointing task

## Slide 17: User Study
Task 1: Hand Posture Rating
Generate random hand posture, check with naïve metric and show subject
Subject has to mimic hand posture
Subject has to rate hand posture on a intuitive comfort/discomfort scale from 0 to 10
Beforehand: show relaxed and extremely uncomfortable hand posture for reference

## Slide 18: User Study
Task 2: Target Shooting
Again show subject randomly generated hand posture
Again mimic and rate
Subject has to perform target shooting test using that posture
Track palm pose with infrared marker tracker t
Track hand posture with Leap Motion Controller
Measure for performance: total task completion time

## Slide 19: User Study
Main User Study:
Hand Posture Rating, used for improving the metric
Target Shooting, used to investigate impact of comfort/discomfort on performance
Verifying the metric:
Extra round of Hand Posture Rating

## Slide 20: Results: Verifying Hand Posture Rating
Pearson Correlation: -0.748993, p-value: 5.89e-12
  Improved metric reflects perceived user comfort/discomfort

## Slide 21: Results: Target Shooting
Pearson Correlation: -0.6651999, p-value: 6.73e-9
Indicates that comfort/discomfort affect performance

## Slide 22: Conclusion
1. Creating a Comfort/Discomfort Metric
Goal: Metric for quick, objective hand posture evaluation
Creation based on
  Existing Concepts
  Comfort/Discomfort Models
  Hand Anatomy and Ergonomics
Tweaked the metric using data from a user study
Verified the metric in a testing user study

## Slide 23: Conclusion
2. Showing Importance of Metric
Goal: Show Comfort/Discomfort-Performance Correlation
Tested in Target Shooting Task
Test Results indicate that hand posture comfort/discomfort do affect performance

## Slide 24: Future Work
Limits of this work:
Early, potentially incomplete model
Combined Comfort and Discomfort
Only short-term effects
Develope more sophisticated models
Investigate Comfort and Discomfort seperately
Investigate short- and long-term effects

## Slide 25: Acknowledgements
Nicholas Schneider
Dr. Frieder Pankratz

## Slide 26: Questions?

## Slide 27: Appendix

## Slide 28: Results
Training Data: Improved Metric and User Rating
Pearson Correlation: -0.6453242
p-value: < 2.2e-16
Not perfect:
  Anatomical and psychological differences
  Short term effects only
  Few discrete steps

## Slide 29: Results
Test Data: Naive Metric and User Rating
Pearson Correlation: -0.6651999
p-value: 6.73e-9
No big difference on first sight
However, standard error is smaller, better correlation